## Slide 1: University Astronomy
Professor Don Figer
Telescopes I

## Slide 2: Aims and outline for this lecture
describe
  history of telescopes
  optics
  properties of telescopes
  modern telescope systems

## Slide 3: telescope systems

## Slide 4: Backyard Telescope

## Slide 5: The First Telescopes
Hans Lippershey got the patent for the telescope.
Galileo first used telescope for astronomy.
He was first to see sunspots, moons of Jupiter, phases of Venus.
Most astronomical discoveries since have involved telescopes.

## Slide 6: Modern Telescope System
Opto-mechanical and thermal control
Acquisition & guiding
Telemetry and sensing
Instrumentation and instrument interfaces (ports)
Software for telescope and instrument control
Technical support and maintenance
Data storage and transfer
Software pipelines for data reduction and analysis
Environment for observer and operator
Personnel management, technical and scientific leadership

## Slide 7: Telescope Parameters
Collecting area is most important parameter, and scales as aperture diameter squared (A=pr2).
Length is a practical parameter that impacts mass and dome size.
Delivered image quality (DIQ) is a function of optical design, manufacturing aberrations, and observing site.
f/ratio determines plate scale and field of view.
Notes: The photo shows the Yerkes 40 inch refractor. Note that the floor has been raised to nearly the highest level. If one is not careful, it is possible to drive the telescope into the ground.

## Slide 8: Question
How does the collecting area of a 10-meter telescope compare with that of a 2-meter telescope?
a) 5 times greater
b) 10 times greater
c) 25 times greater
d) 50 times greater
vote!

## Slide 9: Answer
How does the collecting area of a 10-meter telescope compare with that of a 2-meter telescope?
a) 5 times greater
b) 10 times greater
c) 25 times greater
d) 50 times greater
vote!

## Slide 10: Telescope Size and Angular Resolution
Ultimate limit to resolution comes from interference of light waves within a telescope.
Larger telescopes are capable of greater resolution because there’s less interference.

## Slide 11: Telescope Size and Angular Resolution
The rings in this image of a star come from interference of light waves.
This limit on angular resolution is known as the diffraction limit.

## Slide 12: Question
Suppose two stars are separated in the sky by 0.1 arc-second. If you look at them with a telescope with an angular resolution of 0.01 arcsecond, what do you see?
a) two distinct stars
b) one point of light that is the blurred image of both stars
c) nothing at all
vote!

## Slide 13: Answer
Suppose two stars are separated in the sky by 0.1 arc-second. If you look at them with a telescope with an angular resolution of 0.01 arcsecond, what do you see?
a) two distinct stars
b) one point of light that is the blurred image of both stars
c) nothing at all
vote!

## Slide 14: Telescope Size and SNR
The ability to detect an object with a telescope is related to the signal to noise ratio (SNR).
The higher the SNR, the easier it is to detect the object.
In source shot noise limited case, SNR goes as telescope diameter.
For faint sources, i.e., read noise limited case, SNR goes as telescope diameter squared.

## Slide 15: Bending light

## Slide 16: Refraction
Refraction is the bending of light when it passes from one substance into another
Your eye uses refraction to focus light

## Slide 17: Focusing Light
Refraction can cause parallel light rays to converge to a focus

## Slide 18: Digital Cameras
A camera focuses light like an eye and captures the image with a detector
The CCD detectors in digital cameras are similar to those used in modern telescopes

## Slide 19: refracting and reflecting telescopes

## Slide 20: Refracting/Reflecting Telescopes
Refracting Telescope: Lens focuses light onto the focal plane.
Reflecting Telescope: Concave mirror focuses light onto the focal plane.
Almost all modern telescopes are reflecting telescopes.

## Slide 21: Disadvantages of Refracting Telescopes
Their lenses sag.
They need long tubes.
Chromatic aberration: Different wavelengths are focused at different focal lengths (prism effect).
Can be corrected, but not eliminated by second lens out of different material.
Difficult and expensive to produce: All surfaces must be perfectly shaped; glass must be flawless; lens can only be supported at the edges

## Slide 22: Reflecting Telescopes
Most modern telescopes use mirrors, they are “reflecting telescopes.”
Chromatic aberrations eliminated, i.e. they are “achromatic.”
Fabrication techniques continue to improve.
Mirrors may be supported from behind.
Mirrors may be light-weighted, and thus may be made much larger than refractive lenses.

## Slide 23: Lightweight Mirrors
Telescope primary mirrors can be made lighter by removing material from the back.
Once made thinner, the mirrors can easily be deformed by pushing on the back side.
These mirrors are easier to point and reach thermal equilibrium more quickly.

## Slide 24: optical configurations

## Slide 25: Basic Designs of Optical Reflecting Telescopes
Prime focus: light focused by primary mirror alone
Newtonian: use flat, diagonal secondary mirror to deflect light out side of tube
Cassegrain: use convex secondary mirror to reflect light back through hole in primary
Nasmyth (or Coudé) focus (coudé  French for “bend” or “elbow”): uses a tertiary mirror to redirect light to external instruments (e.g., a spectrograph)

## Slide 26: Prime Focus
Sensor
Mirror diameter must be large to ensure that
obstruction does not cover a significant fraction of
the incoming light.
F

## Slide 27: Newtonian Reflector
Sensor

## Slide 28: Newtonian Reflector

## Slide 29: Cassegrain Telescope
Sensor
Secondary
Convex Mirror

## Slide 30: Feature of Cassegrain Telescope
Long Focal Length in Short Tube
Location of
Equivalent Thin Lens
f
Tube

## Slide 31: Schmidt-Cassegrain Telescope

## Slide 32: Schmidt-Cassegrain Telescope

## Slide 33: Coudé or Nasmyth Telescope
Sensor

## Slide 34: Nasmyth Mount

## Slide 35: Reflecting Telescopes

## Slide 36: Plate Scale
F=focal length
q
x

## Slide 37: Field of View
Two telescopes with same diameter, different F#, and same detector have different “Fields of View”:
Small F#
Large F#
large 
small 

## Slide 38: Eyepieces

## Slide 39: big telescopes

## Slide 40: Big Telescopes
Collecting power scales as the square of the diameter, so big telescopes can see fainter things.
The ability to see fine detail scales as the diameter of the telescope, so bigger telescopes can see objects that are closer together (although, the atmosphere can mess that up).
Because of these two factors, astronomers always want to build bigger telescopes.

## Slide 41: Big Telescopes Sometimes have Segmented Mirrors

## Slide 42: Big Telescopes Have Absurd Names

## Slide 43: History and Future of Telescope Size

## Slide 44: Optical Telescopes: Resolution

## Slide 45: Optical Telescopes: Collecting Area
Notes: ORM is now the Gran Canary Telescope (GTC).