## Slide 1: W.M. Keck Observatory Update
Randy Campbell
Notes: SA, specializing in AO science operations
Past , Present, and Future

## Slide 2: 2013: 20th Anniversary of Science Operations
Keck 1, 1988
First Light Nov 1990
Engineering Camera
with 9 segments
Photo Courtesy of Gerry Smith, Keck Project Manager
Notes: First light image with an engineering camera
Successful demonstration led to approval and funding (W.M. Keck foundation) for Keck II

## Slide 3
First Science instrument image 17 Mar 1993
First Instrument, NIRC
All 36 segments
Detector:
  2562 InSb SBRC
Sensitivity, Ks = 23.83
  (SNR = 5, Tint=3600, Aperture = 0.5”)
  (MOSFIRE Sensitivity, Ks = 23.89)
  Keith Matthews awarded the American Astronomical Society’s (AAS) Joseph Weber Award for Astronomical Instrumentation for 2013.
D79 (Dewar#79) Log Book

## Slide 4: 20th Anniversary
  HQ Open House
    ~2500 participants
    60 exhibits
  Science Meeting
  VIP Gala
Notes: I manned the IR Camera station where we took thermal images of visitors,
Using a fluke device with a microbolometer array, operates at room tempeture, cost less than $10k

## Slide 5: Current Instruments
Keck I
  LRIS, multi-object spectrometer, imager
    PI’s Judy Cohen, Bev Oke CalTech
    Blue: 2x2Kx4K E2V, Red: 2x2Kx4K LBL
  HIRES, High Resolution Echelle Spectrometer
    PI Steve Vogt, UCSC
    CCD: MIT-LL 2Kx4K
  OSIRIS, AO fed, IR integral field spectrometer
    PI James Larkin UCLA
    Spectrograph: Hawaii 2, Imager, Hawaii 1
  MOSFIRE, IR multi-object spectrometer, imager
    PI’s Ian McLean UCLA, Chuck Steidel CalTech
    Hawaii2RG
  NIRC, decommissioned 2010
    PI Keith Matthews CalTech
OSIRIS moving to Keck 1, 2012
Notes: K1 LGS in into its second semester of Science Operations with OSIRIS, moved over from Keck II

## Slide 6: Current Instruments
Keck II
  DEIMOS, multi-object spectrometer, imager
    PI Sandra Faber UCSC
    8x2Kx4K E2V
  ESI, high resolution Echelle spectrometer
    PI Joe Miller UCSC
    2Kx4K E2V
  NIRC2 (D82), AO fed, IR imagers/spectrometer
    PI Keith Matthews CalTech
    Aladdin III InSb 1Kx1K
  NIRSPEC , IR high resolution Echelle spectrometer
    PI Ian McLean UCLA
    Aladdin III InSb 1Kx1K
    NIRSPAO when used with Adaptvie Opitics
Keck-Keck Interferometer, decommissioned 2012

## Slide 8: NGAO Next Generation AO
Improved near-IR performance
  Strehls  80% at K)
  Improved PSF stability & knowledge
AO correction at red wavelengths
  Strehl of 15 - 25% at 750 nm
Increased sky coverage
7 LGS Asterism
Major Goals
Notes: Take advantage of developments in
tomographic wavefront reconstruction
MEMS and other deformable mirrors
Sodium lasers
Computing power
Photometry to 5%
100 micro” astrometry
But this is not yet fully funded but Pieces of it are in development

## Slide 9
Center launch telescope for Keck II
TOPTICA / MPB / ESO Fiber Laser
(D. Bonaccini Calia, 2010)
AO Development
Laser table on
elevation ring
Laser Head
Notes: The Dye laser will be replaced in 2014 with a 20W continuous-wave Raman fiber-amplifier laser being fabricated by a consortium of TOPTICA Photonics AG and MPB Communications Inc
The infrastructure and launch system is capable of operating 3 lasers to create a 7 laser spot asterism

## Slide 10
Near IR Tip/Tilt Sensor
10
H2RG
  ARC electronics
Differential Multi-Accumulate Readout
  (Smith and Hale, 2012)
Dichroic Pickoff Stage
OSIRIS
ROIs
Camera Dewar
Top View
Notes: LGSAO performance is sometimes limited by TT
Keck / CalTech project, CIT providing the camera, see Roger’s talk?
AO correction on IR tt star boosts performance
Eng grade H2RG
A technology stepping stone to NGAO
Differential Multi-Accumulate Readout, Roger Smith and David Hale

## Slide 11
PSF Reconstruction
2 projects with overlapping goals:
Field Dependent PSF,
  A. Ghez, UCLA
On-Axis PSF, Keck,
  P. Wizinowich, WMKO
Notes: Not understanding the PSF is one of the biggest limitations of AO science.
It takes away from the precision of photometry, astrometry, and the morphology of resolved objects

## Slide 12
New for 2014
NIRES (D85)
  PI: K. Mathews
  Single setting
  1.0 - 2.5 μm spectral coverage
  H2RG
  ARC electronics
OSIRIS upgrades
  Grating replacement
  Throughput improved
  x 1.5 in J,H
  x 2.5 in K
  H2RG with sidecar
    2014
Notes: NIRES , pi Matthews, D85

## Slide 13: Keck Cosmic Web Imager,KCWI PI: Chris Martin, CalTech
k
Nod and Shuffle
CCD: e2v 4Kx4K
Notes: Integral field spectrometer based on an image slicer design
Red and blue channel, Blue channel is being developed first
E2v CCD, ARC electronics

## Slide 14: LGS Safety Transponder Based Aircraft Detection, TBAD
TBAD bore sighted on the
Keck II secondary
Shutter laser when the ratio
Narrow Beam Signal
Wide Beam Signal
> threshold
Coles and Murphy, UCSD
PASP 2012
Notes: The first automated laser safety system approved by the FAA
1090 +/- 3 MHz with a pulse coded response
Operate without spotters on Keck II starting Friday

## Slide 15: Thanks