## Slide 1: DCDS for roundtable
Paul Jorden
10 Oct 2013
Scientific Detector Workshop, Florence
e2v Matthew Bastable and others
RAL Matthew Clapp and others

## Slide 2: The motivation
Integrated Focal Plane Electronics
  Readout electronics for large focal plane arrays
  Prototyping a test systems using DCDS.
JPAS focal plane 224 signal channels
Digital Correlated Double Sampling (DCDS)
  Moves a significant proportion of the signal processing into the digital domain
  Minimise complexity and size of analogue electronics

## Slide 3: DCDS Processing
Limited to sampling the settled output voltage
Sample frequency/pixel frequency > 14
  16-bit accuracy
  System bandwidth at ADC nyquist frequency
  10% clamp period

## Slide 4: Video Chain
Digital Correlated Double Sampling (DCDS)
DC restore
Anti-alias filter
Single ended to differential
Remove reset feed-through
OversamplingADC
CCD
Video signal conditioning
DCDS
Video Data
OS
DOS
Digital low pass filter
Correlated double sampling
Analogue
Digital
Reference samples (ri)
Signal samples (si)
ADC output (ADU)
CCD OS
20V

## Slide 5: DCDS Prototype
DCDS
Video Card
SDO CEB
CCD203

## Slide 6: Concept for J-PAS
Use differential signals for best common-mode noise rejection
Get √2 noise increase
Use DCDS for optimal noise of system
  100 MHZ sampling frequency; 500 kHz pixel rate
  DCDS better than analogue CDS and recovers some of the loss of differential mode.
References
Clapp SPIE 2012, 8453-49 DCDS
Jorden et al. SPIE 2012, 8453-20. J-PAS