## Slide 1: THE CCD RIDDLE REVISTED: SIGNAL VERSUS TIME – LINEAR SIGNAL VERSUS VARIANCE – NON-LINEAR
Mark Downing, Peter Sinclaire. European Southern Observatory ESO (http://www.eso.org)
But CCDs are suppose to be near perfect compared to …..

## Slide 2: Previous results concluded….
“Sharing of electrons” between pixels that increase as more electrons are collected

## Slide 3: More evidence gathered…PSF
Slope
Y-intersect
PSF linearly degrades with signal.
Both value and change with signal improve as 1/collection phase voltage.

## Slide 4: Mechanism behind “Charge Sharing” between Pixels
Pixel
400nm
Collection Phase
Electric
Field Extent
CCD
Front side
Undepleted Region

## Slide 5: 100% agreement between non-linearity in PTC and correlation between pixels
Signal2 term
Both slope and correlation between pixels vary linearly with signal
Slope
Slope
Both slope and signal2 term
vary with 1/collection phase voltage.

## Slide 6: PTC can be 100% corrected for correlation between pixels by using autocorrelation variance – most accurate method to determine gain

## Slide 7: On going……
Confirm that the effect can be predicted by taking two flat fields and by using autocorrelation to calculate the correlation and thus determine the PSF Vs Signal. Corrections can then be applied to image data.
Consult the experts to better understand the cause of the effect and hopefully find a solution.

## Slide 8: Thank You