## Slide 1: DETECTOR CHARACTERIZATION FOR THE SuMiRe PRIME FOCUS SPECTROGRAPH (PFS)
Murdock Hart , Robert H. Barkhouser, and Stephen A. Smee
Department of Physics and Astronomy, Johns Hopkins University, Baltimore, MD, 21218
Test Cryostat
Sub-Pixel Illumination
Zemax spot diagrams showing the ability of the sub pixel illuminator to image a spot through a 13 mm thick vacuum window. On the Left shows that the addition of the vacuum window degrades the spot size to nearly 75 μm in diameter. On the right shows that with the addition of a null lens we are able to image a spot 2 μm in diameter.
Detector Coplanarity
Flat Fielding
Wenzel XO-Orbit 87 CMM
Micro-Epsilon confocalDT 2405 white light confocal microscope
Coplanarity / topography measurements
Sub-pixel illumination
  Charge diffusion
  Charge transfer efficiency
  Persistence / reciprocity
Labsphere LRS-12Z integrating sphere
Horiba ihr320 monochromator
Newport optical bench
Photon transfer curve
  Read noise
  Gain
  Full well
  Linearity
Charge transfer efficiency
  Extended pixel edge response
Quantum efficiency
Fe55 x-ray source
  Gain
  Charge transfer efficiency
  Charge diffusion
4 identical spectrographs consisting of 3 channels each
    Each receiving 600 fibers from the 2400 at the prime focus
    3800 Å – 6500 Å
    6300 Å – 9700 Å
    9500 Å – 12600 Å
Vacuum Schmidt cameras for each channel
    Fast ƒ/1.1 focal ratio
    1.1” @ ƒ/1.0 projects to 54 μm at focal plane ~4 pixels
  Visible channels use Hamamatsu 2k x 4k 15 μm pixel full-depleted CCDs
    Each channel will use one pair
    Red and blue optimized chips
    170 K operating temperature
  Near Infrared Channel uses Teledyne H4RG-15 HgCdTe 4k x 4k 15 μm pixel
    110 k operating temperature
CCD Specifications
Measure / characterize detectors at cryogenic temperatures
Further evaluation of cryo-cooler active damping system
Test prototype camera electronics
  Pre-amp board
  Front End Electronics (FEE)
  Back End Electronics (BEE)
Hyper Suprime-Cam (HSC) detector specifications
Mitutoyo 10x infinity corrected NIR objective
Mitutoyo infinity corrected tube lens
20 μm pinhole
PFS Spectrograph