## Slide 1
Superconducting Optoelectronics for
Quantum and Neuromorphic Processing
Alex Tait
Faint Photonics Group Sae Woo Nam
Quantum Nanophotonics Group Rich Mirin
Photonics for Quantum Workshop – January 25, 2019
Rochester Institute of Technology

## Slide 2: Is nature predictable, in theory?
  Copenhagen interpretation
  Probably not, and
  in either case, the math is elegant
  - Bohr, Heisenberg
  Local realistic interpretation
  Yes, there is a deterministic theory beneath quantum mechanics
  - Einstein:
  “God does not play dice”
Notes: If you learned quantum mechanincs after 1930, you learned the Copenhagen interpretation, but it has never really been proven

## Slide 3: disproving local realism
Local realism is testable
  John Bell, 1975
Local realism is false
  Hensen et al., 2015
  Giustina et al., 2015
  Shalm et al., 2015 (NIST)
Bell test can generate provably unpredictable random numbers
  Bierhorst et al., 2018
B. Hensen et al., “Loophole-free Bell Inequality Violation Using Electron Spins Separated by 1.3 Kilometres,” Nature 526, 682 (2015).
M. Giustina et al., “Significant-Loophole-Free Test of Bell's Theorem with Entangled Photons,” Phys. Rev. Lett. 115, 250401 (2015).
L. K. Shalm et al., “Strong Loophole-Free Test of Local Realism,” Phys. Rev. Lett. 115, 250402 (2015).
Bierhorst et al., “Experimentally generated randomness certified by the impossibility of superluminal signals,” Nature 556, 7700 (2018).
Boulder campus
entangled photons
Notes: A bell tests involves making entangled particles, separating them far enough so they cannot conspire in some way, then measuring their states’ correlation over many trials.
Local realism predicts that there is a maximum correlation possible. Demonstrating a higher correlation violates local realism.
It also means that we live in a world where there is true randomness.
The data you measure could not have been predicted, even given complete knowledge of the state and history of the universe
It turns out a lot of quantum communication/computing protocols rely on some minimum detection efficiency

## Slide 4
God’s Dice
http://beacon.nist.gov
Random key generation is central to
  Cybersecurity
  E-commerce
  Voting machines

## Slide 5: neeDs for single Photon detection
Bell test
  >67% detection efficiency
Linear quantum computing
  >99% detection efficiency
Quantum communication
  Photon loss -> redundancy -> vulnerability
This is not comprehensive...
Notes: .9^10 = 35%

## Slide 6: outline
Single photon detectors and quantum information
Cryogenic silicon photonic integration
Superconducting Optoelectronic Networks platform
Neuromorphic photonics and quantum photonics

## Slide 7: Single photon detectors
Notes: Foundation of our particular group at NIST

## Slide 8: single photon detection at NIST
Advance science of measuring single photons
Characterize single-photon sources
Transfer detector technology to the public
Investigate new applications
Collaborate
Sae Woo Nam
Contact
saewoo.nam@nist.gov
rich.mirin@nist.gov
jeffrey.shainline@nist.gov
alexander.tait@nist.gov
Notes:   Point 2: All of the components in the characterization setup must be characterized precisely. This is active research
  Point 4: Ultimately our mission is to bring the impacts of science and technology to public society, not just conduct science. We want to share our stuff

## Slide 9: Transition Edge Sensor (TES)
Absorber, C
Thermometer
Weak thermal link, g
Thermal sink
(50 mK)
Energy
deposition
R
T
Rn
~8 W
~1 mK
~0.2 mK
~0.2 W
Calorimetric detection
UV/visible/IR photons
Superconducting
transition edge

## Slide 10: Transition Edge Sensor (TES)
25 mm
Nb wires
Tungsten
(W)
805 nm: ηSystem = 97.7 ± 1.5 %
Goal 2: decrease this number
Goal 1: increase this number
Notes: Very clear difference between 1 photon and 0 photons
We are trying to get that to 99.9%.
Measurement accuracy is something we are trying to improve.
Imagine instead of detecting 2 photons, your QI protocol needs to detect 10 photons at a time.

## Slide 11: superconducting nanowire Single-photon detector (SNSPD)

## Slide 12: system detection efficiency
Device chip
Zirconia sleeve
Fiber ferrule
Sapphire rod
Coaxial connector pin
Miller et al., Opt. Express (2011)
Optical fiber
Notes: If you want to buy, contact them.
If you want to learn, contact us.
there is no secret

## Slide 13: Cryogenic silicon photonics

## Slide 14: Co-integration: waveguides + SNSPDs
Shainline et al. ” Room-temperature-deposited dielectrics and superconductors for...” Op. Ex. 25 10322 (2017).
1 um
Jeff Shainline
Notes: No dark counts
High yield
Photonic routing

## Slide 15: All-silicon light emitting diodes
S. M. Buckley et al. “All-silicon light-emitting diodes waveguide-integrated with superconducting single- photon detectors ” Applied Physics Letters, 111 (14). 2017.
Sonia Buckley
Some Si defects have an optical transition
Low temp. inhibits non-radiative decay
Electrical pumping with PN junction
Notes: Describe the fabrication briefly

## Slide 16: optimizing emission on 12 inch wafers
Implanted at SUNY Poly
Measured at NIST
Photoluminescence
Si+
300mm
Recent results
50x enhancement from prior runs
Evidence of localization in device layer, not handle layer
Pops
Consistent (±10%)
up to 35 Kelvin
Notes: Just verbally talk about etch away tests

## Slide 17: Co-integration: Silicon LEDS + SNSPDS
S. M. Buckley et al. “All-silicon light-emitting diodes waveguide-integrated with superconducting single- photon detectors ” Applied Physics Letters, 111 (14). 2017.

## Slide 18: Superconducting amplifiers
Interface: superconductor signals to semiconductor readout
millivolt input -> Volt output
No Josephson Junctions
A. McCaughan et al. “A compact, ultrahigh impedance superconducting thermal switch for interfacing superconductors with semiconductors and optoelectronics,” Submission pending government reopen. 2019
Adam McCaughan

## Slide 19: The SOEN platform
Superconducting OptoElectronic Networks

## Slide 20
NIST is opening this process to the public
Silicon passives
Superconducting amplifiers
Silicon light sources
Single-photon detectors

## Slide 21: Multi-project wafer format
Fabricated in NIST cleanroom
  3” wafers, 1x1 cm die
  220nm SOI device layer
Process design kit
  Open-access, open-source
  Online (pending govt. reopen)
Preferred design tools
  KLayout (free software)
  phidl (open-source)
3”
www.klayout.de
github.com/amccaugh/phidl
Notes: You can use other design tools of your choice. Maybe “supported” should be “preferred.
Make a point: we want academics and small companies to be on equal footing with large companies. Hence the way we are releasing it.

## Slide 22: More complex systems
Complex systems are enabled by
  High yield
  Electrical-in/Electrical-out
High Dynamic Range Detector Array [1]
  Consistent splitting and efficiency
  No discrete optics or fibers
S. M. Buckley et al. “All-silicon light-emitting diodes waveguide-integrated with superconducting single- photon detectors ” Applied Physics Letters, 111 (14). 2017.
LED
Nanowire response
Nanowire index
Fit lines
Notes: 36 SNSPDs working of 36 tested

## Slide 23: example: photon pair generation
[1, 2, 3]
[1] Cale M. Gentry et al. “Quantum-correlated photon pairs generated in a commercial 45nm complementary metal-oxide semiconductor microelectronic chip,” Optica, vol. 2, pp. 1065–1071, 2015.
[2] Marc Savanier, Ranjeet Kumar, and Shayan Mookherjea, “Photon pair generation from compact silicon microring resonators using microwatt-level pump powers,” Op. Ex, vol. 24, pp. 3313–3328, 2016.
[3] Xiyuan Lu et al., “Chip-integrated visible-telecom photon pair sources for quantum communication,” arXiv: 1805.04011, 2018.
Detectors
Buffers
Sources
Notes: SAY: Our group makes a lot of single photon sources.
We are very interested in single photon sources.
Thinking about quantum dots

## Slide 24: What can you come up with?
Sources
Detectors
Buffers
Silicon Photonic
Quantum Information
Circuit
Notes: SAY: Our group makes a lot of single photon sources.
We are very interested in single photon sources.
Thinking about quantum dots

## Slide 25: We are looking for collaborators
With expertise in integrated photonic device measurement
  Cryogenic temperatures
  High speed
Have new ideas for applications in
  Quantum information science
  Measurement science
  Neuromorphic Photonics
Willing to design characterization structures and report findings
  Detectors
  Sources (esp. single photon)
  Passives
Contact
jeffrey.shainline@nist.gov
alexander.tait@nist.gov
saewoo.nam@nist.gov
rich.mirin@nist.gov
Notes: Is it accurate to say public access will be 2020?

## Slide 26: Neuromorphic Photonics

## Slide 27: Neural networks in computing
Today, there is large demand to perform neural network operations
Conventional computers are inefficient at doing these operations
. . .
argmax
Neural network: distributed
Conventional computer: centralized
Notes: Blow through this slide

## Slide 28: Neuromorphic hardware
Specialized distributed hardware
Does neural network operations
High communication cost
  Energy
  Time
[1] F. Akopyan et al, “TrueNorth: Design and tool flow of a 65 mW 1 million neuron programmable neurosynaptic chip,” 2015.
[2] S. B. Furber et al. “The SpiNNaker project,” May 2014.
Robotics, supercomputing
Based on synaptic cross-bars
. . .
Weights
Sum
∑
∑
Nonlinearity
Broadcast
Notes: At the end: Make the argument: connectivity -> photons; efficiency -> single photons

## Slide 29: Superconducting optoelectronic networks
J. M. Shainline et al., “Superconducting optoelectronic circuits for neuromorphic computing,” Phys. Rev. Applied, vol. 7, p. 034013, Mar 2017.
J. Chiles et al., “Design, fabrication, and metrology of 10x100 multi-planar integrated photonic routing manifolds for neural networks,” APL Photonics, vol. 3, p. 106101, 2018/08/08 2018.
. . .
Weights
Sum
∑
∑
Nonlinearity
Broadcast
Jeff Chiles
beam tap
Detect
Amplify
Transmit
Cryogenic temperatures
Extremely low power dissipation
Goal: Maximum scalability
SOEN neuron

## Slide 30: silicon photonic neural networks
[1] A. Tait, M. A. Nahmias, B. J. Shastri, and P. R. Prucnal, “Broadcast and Weight: an Integrated Network for Scalable Photonic Spike Processing,” J. Lightwave Technol., 32(21), 2014.
[2] A. Tait, T. Ferreira de Lima, E. Zhou, A. X. Wu, M. A. Nahmias, B. J. Shastri, and P. R. Prucnal, “Neuromorphic Photonic Networks Using Silicon Photonic Weight Banks.” Scientific Reports, 7(1). 2017.
[3] A. Tait, T. Ferreira de Lima, M. A. Nahmias, H. B. Miller, H.-T. Peng, B. J. Shastri, and P. R. Prucnal
“A silicon photonic modulator neuron.” arXiv preprint:1812.11898. Dec. 2018.
V+
V–
GND
Ih
Ib
photodetector (PD+)
Al wires
Si WGs
MRR modulator
Heater
Ge
IN+
IN–
Out
Pump
50µm
photodetector (PD–)
neurons
weight matrix
25 µm
DROP
THRU
IN
d)
Silicon photonic neuron
MRR weight bank
[1]
[3]
[2]
Electro-optic nonlinearity
10 – 40 GHz operation
Foundry compatible

## Slide 31: Next steps: hierarchical Networks
Large neural networks are hierarchical
Photonics does well with long-range communication
How do we design chip-scale systems? wafer scale? datacenter scale?
[1] Paul Prucnal and Bhavin Shastri. Neuromorphic Photonics. CRC Press, 2017.
[2] J. M. Shainline et al. “Superconducting Optoelectronic Neurons V: Networks and Scaling,” arXiv:1805:01942, 2018.
Neuron # (x 10-3)
Neuron # (x 10-3)
[2]
region
module
[1]
connection matrix
layout rendering
Notes: The “how do” leads into the next slide

## Slide 32: large-scale silicon photonic systems
Basic component quality
Large-volume manufacturability
Small-volume research prototyping
Challenges to quantum and neuromorphic computing are shared
Notes: Why is silicon photonics the way it is?
Demand for quantum computers? No

## Slide 33: large-scale silicon photonic systems
Basic component quality
Large-volume manufacturability
Small-volume research prototyping
[1] The Cattington Post
Challenges to quantum and neuromorphic computing are shared
Externalized technological risk
(thanks to Datacomm.)
Notes: It’s demand for cat videos.
Datacenters need fiber optics and lots of cheap optical receivers and transmitters
That industry invested in silicon photonics. The demand is not going away
That is externalized technological risk.
It is unprecedented in the history of optics to have a stable platform technology

## Slide 34: large-scale silicon photonic systems
Basic component quality
Large-volume manufacturability
Small-volume research prototyping
Challenges to quantum and neuromorphic computing are shared
Semi-externalized
I/O, packaging
System-level design tools
Process variation
Control complexity
Heat dissipation density
Specific to large-scale systems
Externalized technological risks
(thanks to Datacomm.)
Notes: BUT, where it gets hard is where the needs of large-scale depart from those of data communication.
That’s where we need to work together "Going to make a sentence point on each one”

## Slide 35: summary
Quantum and Neuromorphic share platform technologies
Co-integrated passives, sources, amplifiers, SPDs
This platform will become available to the public
NIST trying to advance single photon devices, metrology, and applications

## Slide 36: NIST team
Sae Woo Nam
Rich Mirin
Jeff Shainline
Sonia Buckley
Adam McCaughan
Jeff Chiles
Alex Tait
Saeed Khan
Krister Shalm
Marty Stevens
Adriana Lita
Varun Verma
Nima Nader
Mike Mazurek
Dileep Reddy
Eric Stanton
Galen Moody
Kevin Silverman
Thomas Gerrits
Boulder Labs
Postdoctoral
opportunities
Contact
saewoo.nam@nist.gov
rich.mirin@nist.gov
jeffrey.shainline@nist.gov
alexander.tait@nist.gov
atait@ieee.org