## Slide 1
Shayan Mookherjea
UC San Diego, Micro/Nano-Photonics Group
http://mnp.ucsd.edu
Very-Fast Photon Sources and Detectors
PfQ Workshop, Jan 2019

## Slide 2
Outline
2. We develop and study silicon photonics & 3D technologies:
  Entangled photon pair generation, filtering and routing using silicon photonics
  InP-on-Si lasers, and LN-on-Si modulators, through bonding,
  Uses, and can be packaged with, microelectronics.
We use foundry fabrication, including multi-project wafer runs, as far as possible, and develop new solutions where needed.
1. Explanation of what I mean by “very-fast …”
  … entangled-photon sources
  … single-photon detectors

## Slide 3
Very-fast versus ultra-fast …
[Sources] Speed up each “trial” i.e., use of the resources in the quantum channel (pump, modulator, …, detector gate).
[Detectors] Detect (very) broadband waveforms at (very) low powers, e.g., a sampling oscilloscope.
Femtosecond pulses
Dynamics of electrons, excitons etc.
(Repetition rates ~ 100 kHz - 100 MHz)
[ this term is already in wide use ]

## Slide 4
What is a “trial”?
In communications, a “trial” is often called “channel use”.
e.g., Discrete-time Gaussian Channel capacity:
E = average energy of the received symbol
s = st. dev. of noise (iid random variable)
Given the rate of trials, e.g., one channel use per microsecond, we can calculate the usual Cbps, capacity in bits per second.
Integrated optics can improve “per channel use” rate by 100 -1000 x.
bits per channel use

## Slide 5
Quantum Key Distribution
Transceiver for quantum state
Nordholt & Hughes, Los Alamos Science (2002)
Sangouard et al., Rev Mod Phys (2011)
Metcalf … Walmsley et al., Nature Photonics (2014)
Completion time is proportional to time needed per bit / attempt i.e., “trial”

## Slide 6
Time to distribute a single entangled photon pair ( seconds )
A : direct transmission
A: Single photon source: 10 GHz repetition rate, Fiber loss 0.2 dB/km, 90% detector efficiency
Quantum Repeater protocols: B : DLCZ protocol, C : entanglement swapping [Jiang et al. 2007], D : Chen et al (2007), E : Simon et al. (2007) photon-pair sources + multimode memories, F : Sangouard et al. single-photon sources (2007), G : Sangouard et al. entangled-pairs
400
500
600
700
800
Distance (km)
1
10
100
1000
Sangouard et al. Rev Mod Phys (2011)
Transceiver for quantum state : entanglement distribution time

## Slide 7
Nonlinear crystal
Pump
Signal
Idler
Louisell et al. (1961)
SPDC, SFWM
Differential noise is suppressed i.e., Var [Ns – Ni] at detector = 0.
Cavity photon lifetime proportional to Lc: make small, efficient cavities for “fast” photons.
Ns
Ni
Lc

## Slide 8
Alain Aspect (1982)
Nicolas Gisin (1997)
?
Photon generation & entanglement creation apparatus
Room-sized
Breadboard-sized
Integrated microchip
kHz
GHz
THz
MHz
m2
mm2
cm2
Trial rate:
Size:

## Slide 9
Requirements to speed up “trials” 10 … 100 GHz
Small devices (e.g., photon lifetime < 100 ps) … natural candidate for integrated optics.
High intrinsic generation rate (highly nonlinear material + phase-matched pair generation process), e.g., Si microring resonators: pair generation rate 150 MHz.mW-2
Ability to use, process & measure upto 100 GHz (approx. 1 nm) bandwidth.
Methods of generating pump pulses, and operating the source that are scalable, manufacturable, parallelizable, low-cost.
Leveraging multi-project wafer shuttles

## Slide 10
Cover article Appl. Phys. Lett. 100:261104 (2012)
Selected as Editor's Picks of 2012, as one of the most notable APL articles published in 2012
Collaboration with NIST and IBM T. J. Watson Labs
“Telecommunications-band heralded single photons from a silicon photonic chip”
Based on microring resonators (in this case, coupled microrings). All wavelengths near 1550 nm. Spontaneous four-wave mixing, with an optical pump beam (mW powers).
Our subsequent experimental work:
Wavelength-division multiplexing with single photons: Optics Letters (2013)
Controlling the entanglement of photons at the source: Nature Communications (2014)
Experimental proof of entanglement (2-photon interferometer): Optics Express (2015)
Temperature-stabilized pair generation using microrings: Applied Physics Letters (2015)
Microwatt-scale pump power pair generation: Optics Express (2016)

## Slide 11
Entangled photon pair generation simultaneously at the 1310 nm and 1550 nm wavelength bands
IoP Quantum Science and Technology, Vol. 3, No. 3, 034001 (2018)
40.037
1310 nm pump
1550 nm pump power ~ 0.1 mW
Franson visibility (1310 nm) 97.4 ± 13.4 %
Franson visibility (1550 nm) 97.8 ± 4 %
1310 / 1550 DEMUX
1 MHz
2 MHz
CAR : 530
CAR : 650
Resonances at both 1310 nm and 1550 nm
wavelength (nm)
wavelength (nm)
Transmission (dB)
Transmission (dB)

## Slide 12
Pair generation without mode-locked lasers
Step recovery diode
Applied Physics Letters, 108, 251102 (2016)
2-terminal p-i-n diode whose junction impedance depends on internal charge storage.
Can generate pulses of a few tens of picoseconds, at approx. GHz rates.

## Slide 13
Photon Pair Generation using Silicon Photonic Microring and Hybrid Laser
CLEO 2017 Post-deadline paper JTh5C APL Photonics, Vol. 3, No. 10, 106104 (2018)
Room temp. pair & heralded single photon generation for data-center applications (at 1310 nm) CAR: 417
Heralded single-photon: g(2)(0) = 0.095 Pair generation rate: 300 kHz at 1 mW pump
Heralding efficiency: ~ 6%
CW, or pulsed.
< 100 mA current, ~ 1 Volt, electrically-pumped hybrid silicon laser [collab. w/ Intel]

## Slide 14
Previous (typical) results (Si Photonics SFWM):
CAR ~ 100 – 1,000
g(2)(0) ~ 0.1
V2-photon ~ 92%
(see Table 1 in paper)
Dec 2017
The spectral brightness (# pairs / s / GHz / mW2) of this device is:
  100x higher than reported by other groups [Ref. 22],
  24x higher than our previous results [Ref. 8],
  2x greater than that of the silicon microdisk [Ref. 7].
Paper also reports entanglement verification through 2-photon Franson interferometer (time-energy entanglement)
1.5 x 108

## Slide 15
tap
Classical 10 Gbps link
ALICE
BOB
Photon pair generation
Pair generation using spontaneous four-wave mixing in a silicon microring resonator
“Pump laser” = [ tap fraction of ] 10 Gbps NRZ data stream. Rest of the 10 Gbps data stream available e.g., for classical link.
No need for separate pump laser!
Optics Express, Vol. 26, No. 18, 22904 - 22915 (2018)
Still need photonics components: polarization control, filters, monitor PD etc.

## Slide 16
Good performance of photon-pair and heralded single photon generation
Microring resonator pumped by 10 Gbit/s NRZ data stream (tap fraction)

## Slide 17
tap
Classical 10 Gbps NRZ link
ALICE
BOB
Photon pair generation
Bit number
Bit number
0
20
(c)
FPGA
switch
coupler
TDC
ΔL
Heralding photon
Time bin encoder
40
60
80
100
300,520
300,560
300,600
-1
0
+1
ns
-1
0
+1
ns
0
40k
80k
clock
data
SPD
SPD
Time-bin encoded single-photon transmission
Microring resonator pumped by 10 Gbit/s NRZ data stream (tap fraction)

## Slide 18
Alice has an image (sequence of bits).
Alice and Bob generate a mutual key over the heralded single photon channel. No basis change at this time.
Alice sends (Original image) XOR (mutual key) to Bob over the classical channel.
Bob decodes using his key.
XOR
Alice’s key
=
XOR
Bob’s key
=
Alice’s original message
Sent over classical channel
Bob’s decoded message
Wavelengths: pump diode : generated photon pair : | 1555 nm 1535 & 1575 nm
Clock for pair generation : Optical pump power used : | 10 GHz -5.5 dBm
Pair gen. rate (Alice) : Photon detection (Bob) : | ~ 5 MHz 20-200 kilo-count/s
Time bin width : | 2 ns
Message size: 188223 bits | QBER 1.9% [ ‘0’, ‘1’ ] = [2.2%, 1.6%]

## Slide 19
Optical Sampling oscilloscope – an application of detectors
Typical equipment:
Keysight DCA-X sampling oscilloscope with optical front-end module.
Cost: $50K, approx.
Min detection power: ~ -20 dBm [10 uW]
Time to acquire nice eye: ~ 0.5 - 1 minute.

## Slide 20
Optical Sampling oscilloscope at femtowatt power levels

## Slide 21
Clock
Dt
single photon detector
How it works:
+1
Dt
histogram

## Slide 22
Clock
Dt
single photon detector
How it works:
+1
Dt
histogram

## Slide 23
Clock
Dt
single photon detector
How it works:
+1
Dt
histogram

## Slide 24
Clock
Dt
single photon detector
How it works:
+1
Dt
histogram
Eventually, the histogram = the waveform being acquired.
More precisely, a sampled version of the waveform, but most waveforms are generated from discrete samples, anyway.

## Slide 25
RF waveform
Optical waveform
New, state-of-the-art
ultrafast electro-optic modulator
New, state-of-the-art
single photon detector
New, state-of-the-art
TCSPC card
Clock
can measure any bandwidth generated by the best-available Arbitrary Waveform Generators, AWG’s [ 92 GSa.s-1 , 32 GHz analog BW ] … at < 100 femtowatts of received power!

## Slide 26
Optical eye diagrams at –100 dBm optical power [ measured at receiver front-end ]
90 GHz
Length to resolution ratio: ~ 4,000
40 GHz
102 GHz
Measurement time: 2 minutes *
* 150 milliseconds enough for identification of signal frequency at 100 GHz.

## Slide 27
Outline
Integrated photonics can be used to :
  reduce the size, weight and power (SWaP) of optical assemblies,
  to improve functionality,
  and improve performance in some cases.
How can collaboration between universities, leveraging foundry fabrication, help? I will present a case study.
What do I mean by “very-fast …
  … entangled-photon sources
  … single-photon detectors

## Slide 28
CIAN: NSF Center for Integrated Access Networks
10-year, $40M+ multi-institutional program
C2.1 Silicon Photonics
Photonic Chip participants:
Cornell (Michal Lipson)
UC San Diego (Shayan Mookherjea [coordinator])
UC Los Angeles (Bahram Jalali)
UC Berkeley (Connie Chang-Hasnain)
University of Arizona (Robert Norwood)
UC Berkeley (Ming Wu)
Caltech (Axel Scherer)
Cornell
UC San Diego
UC Berkeley
UC Berkeley
Univ. Arizona
Sandia National Labs,
Albuquerque, New Mexico
Notes: 28

## Slide 29
Chip V1
2014-15
Chip V2 2015-16
Notes: The first version of the chip was a test platform – it was edge coupled, single polarization, limited tuning range.
We have improved that for the second chip, now being measured.
This is small enough that you can fit it inside the transceiver module.
No extra external fibers to bring ROADMs into a network – a sub-microsecond mini-ROADM can be built into the transceiver itself.

## Slide 30
2. Wideband (> 40 nm) adiabatic directional couplers
Conventional directional couplers in silicon photonics are highly wavelength dependent
Chip design details
3. Integrated variable optical attenuator on each input
50 um length
approx. 5 – 10 mW power
fast (sub-ns)
wide waveguide
narrow waveguide
Current heats the silicon on the inside of the ring
25 um
1. Widened rings + tunable heaters
4. MORDIA has asymmetric add/drop specifications
single 400 GHz tunable drop; multiple 100 GHz tunable adds

## Slide 31
MORDIA
Wide-wavelength-span directional coupler (used in several places)
100 um
C. T. DeRose et al. OFC OThM3 (2011)

## Slide 32
V1, 2013-4
V2, 2015-6
waveguide in
waveguide out
p-dopant
n-dopant
rib-to-ridge waveguide transition
metal contact
50 um
GDS
optical image
15 dB range
35 dB range
X. Wang, et al. "Compact Silicon Photonic Resonance-Assisted Variable Optical Attenuator" Optics Express, Vol. 24, No. 24, 27600-27613 (2016)

## Slide 33
V1
2013-4
V2
2015-6
The net result: improved channel ‘eye’ [10 Gbps NRZ]
Eye SNR = 11 dB
Eye SNR = 9 dB
@ THRU
@ THRU

## Slide 34
MORDIA today
Objectives:
chip-scale integration of:
  tunable drop 4-channel tunable add 4+1 channel VOA (optical power control)
R. Aguinaldo et al. IEEE Photonics Conference, post-deadline paper PD.3 (2014)
4l 40 Gbit/s Add-Drop-VOA Node on-a-Chip
Wavelength (nm)
DROP 4
Si photonic chip
Grating – tilted fiber readout
Edge-coupled fiber array
Si Photonic chip
1.3 mm x 0.5 mm
in, through, add
drop
4 x 10 Gbps ADD
(2^31 – 1 PRBS)
e.g., ITU-T 100 GHz grid channels 22-25 added:
10 Gbps NRZ

## Slide 35
Many positive outcomes
Initiated a (continuing) collaboration between universities and a national lab, under a shared research theme.
More than 25 graduate students and post-doctoral scholars directly worked on layout and measurements. (In most cases, this was their first exposure to photonics TCAD).
Many collaborations with existing companies. Some students hired straight out of PhD (or before). New companies were started, some directly within the ERC, and some in follow-on projects (e.g., 3 from UCSD).
New international collaborations came out of this work.

## Slide 36
Micro/Nano-Photonics at Univ. California, San Diego mnp.ucsd.edu
Government support:
Industry sponsors:

## Slide 37
http://mnp.ucsd.edu
University of California San Diego - La Jolla, California