## Slide 1
Electro-optic Quantum Transduction between Superconducting Microwave Qubits and Optical Photons
Mo Soltani, PhD
Leonardo Ranzani, PhD
Quantum Engineering & Computing Group
Physical Sciences & Systems Department
This document does not contain technology or technical data controlled under either the U.S. International Traffic in Arms Regulations or the U.S. Export Administration Regulations.
Space & Airborne Systems

## Slide 2: Photonics and Superconducting Quantum Technologies at Raytheon BBN
Optics & Integrated Photonics Testbeds
UV/Visible/Telecom Range
Cryogenics
Cryogenic/Superconducting Electronics Labs
Raytheon DOD trusted III-Nitride (GaN) foundry at Andover MA
Access to Harvard Nanofabrication Facility

## Slide 3: Quantum Engineering and Computing @Raytheon BBN
Algorithms
Novel uses of quantum walks for optimization problems
Randomized methods for characterizing circuits
Programming Languages
Quantum Gate Language
Extensive research in higher-level language design
Classical Control
Custom AWGs and Digitizers
Cryogenic digital and microwave circuits
Devices
  Photonic Integrated Circuits
  Novel quantum-limited amplifiers
  Multi-qubit circuits
Multiqubit and amplifier chips circuits
Quantum control circuits
Fabrication and packaging
Qubit specs:
T1 and T2 from 15-25 us
Resonant frequency = 7.1-7.4GHz
  First demonstration of metro area QKD in Cambridge, MA (DARPA Quantum Network Program)

## Slide 4: Interfacing Superconducting and Optical Technology
Quantum Devices
Digital SFQ (logic/ADC)
MMIC
Quantum Packaging
I/O via Optical MUXING,
analog field generation CryoCMOS, limited DSP
Cryomemory
77K
RT
4K
0.1K
0.01K
Cryogenic computing/sensing node A
Cryogenic computing/sensing node B
Coherent quantum state transfer between cryogenic and room temp on fiber
Replacing traditional copper cable I/O with optical fiber for massive classical data transfer
Cryogenic Classical/Quantum Computing
Optical comm for classical/quantum data transfer to remote distance
Dilution fridge

## Slide 5: Quantum Technologies: Superconducting vs. Optical
 | SC Quantum Technology | Optical Quantum Technology
Qubit operation frequency | 5-10 GHz | 193 THz
Operation Temperature | 10 mK | Room temperature
Single photon nonlinearity | Strong (enables high fidelity gates) | Weak
Quantum memory | Yes (tens of microseconds and more) | No
Long distance comm/interconnect | No (stationary qubit) | Yes (flying qubit)
 | Strong candidate for computing | Strong candidate for comm. (~km travel with no need for quantum repeater)

## Slide 6: Pursued Transduction Schemes
Technology | g/2π | Thermal & Mechanical stability | Scalability | Tunability | Comment
Optomechanics | Hz-100 KHz | Low | Low | Low | Suspended, hard to scale
Piezo-mechanics | 50 KHz | Low | Low | Low | Similar to optomechanics
Magnon | 10 Hz | High | Low | Low | Small g < 10 Hz, suspended
Electro-optics | 100 Hz-10 KHz | High | High | High | High g, ultrahigh optical Q (107), moderate microwave Q (103-105)

## Slide 7: Quantum Electro-Optic Transduction

## Slide 8: Example of EO Transduction Schemes
WGM EO Resonators, Harald Schwefel
Oxide substrate
WGM resonator
Si wafer
Si Waveguide
WGM
RF electrode
RF electrodes
Early work of our group in collaboration with OEWaves and IBM
Integrated AlN resonators, Hong Tang (Yale)
Integrated LiNbO3 resonators, Kippenberg (EPFL)

## Slide 9: Transduction using Single WGM Electro-Optic Resonators
optical pump
Microwave cavity
Optical resonator
pump
up conversion
down conversion
Optical FSR
optical
microwave
Optical pump photon number in the resonator
The down-conversion sideband is undesired and a noise term
(*)
*: A. Matsko, et. al. “On fundamental noise of whispering gallery resonators,” Optics Express 15, 17401 (2007).
*: M. Soltani, et. al. “Efficient quantum microwave-to-optical conversion using electro-optic nanophotonic coupled-resonators,” PRA 96, 043808 (2017).

## Slide 10: Transduction using Single WGM Electro-Optic Resonators
optical pump
Microwave cavity
Optical resonator
pump
up conversion
down conversion
Optical FSR
Off-resonance pump though suppresses the down-conversion, heats up the fridge
Optical Q | Microwave Q | g/2π | Pump power (on-resonance) | Pump power (off-resonance)
106 | 105 | 10 kHz | ~3 µW | ~9 mW

## Slide 11: Mechanically Polished WGM LiNbO3 EO Resonators
Oxide substrate
WGM resonator
Si Waveguide
Si wafer
WGM
Laser light
RF electrode
RF electrodes
A. Rueda, et. al., Optica 3, 597 (2016)
Discrete coupling
Si Waveguide
Integrated coupling

## Slide 12: Efficient Coupling Design between Si Waveguide and WGM LN Resonators
SiO2
LT
Δx
Δx (µm)
Coupling Q ( million )
WG-resonator gap (nm)
coupling Q
1 µm
20 µm
air
sio2
400 nm
sio2
air
Oxide substrate
WGM resonator
Si Waveguide
Si wafer
Simulation results showed phase matching and efficient coupling between a Si waveguide WGM Resonator

## Slide 13: Demonstration of Efficient Coupling between Si Waveguides and WGM LN Resonators
Frequency (MHz)
Normalized transmission
Q ~ 180 millions
Q ~ 45 millions
under-coupled
~ critically coupled
3 µm
Si waveguide
Frequency (MHz)
1550 nm
laser light
M. Soltani, et. al. “Ultra-high Q whispering gallery mode electro-optic resonators on a silicon photonic chip,” Opt. Letters 41, 4375 (2016)
Efficient coupling demonstration between a Si waveguide and a WGM LN Resonator (Q~108)

## Slide 14: Migrating to Integrated Nanophotonic EO Resonators
Work of Loncar’s group (Harvard) M. Zhang, et al., Optica 4 (12), 1536–1537 (2017)
LiNbO3
Q ~ 10,000,000
Integrated Ultra-high Q Nanophotonic EO Resonators Results in much higher g factors

## Slide 15: Coupled Nanophotonic EO Resonators
optical pump
Microwave cavity
Optical resonator
pump
up conversion
down conversion
Optical FSR
Optical pump
Supermodes resonances
optical
microwave
Pump
up conversion
Suppressed down conversion
Optical doublet spectrum
This scheme has also been proposed by Milos Popovic in silicon photonics and in classical domain for single sideband modulation
Y. Ehrlischman, et. al. “Dual-cavity resonant modulators for efficient narrowband RF/microwave photonics” IEEE Topical Meeting, Microwave Photonics, 2016
Coupled nanophotonic EO resonator with doublet resonance integrated with a microwave resonator provide an ultracompact triply-resonant system with enhanced g and suppressed down-conversion
Conventional scheme
Our new scheme

## Slide 16: Monolithic Quantum Transduction Chip

## Slide 17: Calculation of g Factor for Nanophotonic Coupled Resonator
LN
W
H
SC qubit circuit
Metal electrode
SiO2
Si
Resonator FSR (GHz)
C > 40 fF
H = 1000 nm
H = 750 nm
g/2π (kHz)
Significant enhancement in g factor (~10 kHz)

## Slide 18: Figure of Merits for Efficient Conversion
Refractive index
EO coeff.
EO mixer
Optical
Microwave
Microwave mode energy
Overlap factor of microwave and optical mode
Microwave E field
optical pump
Intrinsic conversation rate
Cooperativity factor
# pump optical photons in resonators
Optical cavity decay rate
Microwave cavity decay rate

## Slide 19: Figure of Merits for Efficient Conversion
Pump
up conversion
Microwave-to-Optical Quantum Transduction
M. Soltani, et. al. “Efficient quantum microwave-to-optical conversion using electro-optic nanophotonic coupled-resonators,” PRA 96, 043808 (2017)
Efficient and low noise transduction requires the optical and the microwave resonators in overcoupled regime
Optimal conversion occurs at C=1

## Slide 20: Demonstration of Nanophotonic LN Coupled Resonators
M. Zhang, C. Wang, Y. Hu, A. Shams-Ansari, G. Ribeill, M. Soltani, M. Loncar, “Microwave-to-Optical Converter based on Integrated Lithium Niobate Coupled-Resonators,” CLEO 2017
The experimental results show resonance doublet with intrinsic Q ~ 3 millions
20 mm
Loncar group (Harvard)

## Slide 21: Conclusion
Technology: Nanophotonics coupled LN resonator modulator integrated with SC qubits on silicon platform | 
g/2π | ~1-10 kHz
Thermal & Mech. stability | High
Scalability | High
Tunability | High
Any suspended component | No
Required optical resonator Q | 106-107
Required microwave resonator Q | ~10000
Optical pump power | ~ µW
Transduction efficiency | ~>80 %
Fidelity of transferred Fock state | >80 %
Quantum Electro-optic Transduction

## Slide 22: Collaborators & Acknowledgement
Acknowledgement:
  Marko Loncar Group (Harvard)
    Mian Zhang
    Cheng Wang
  Dirk Englund (MIT)
  OEWaves,
  IBM
  Kartik Srinivasan (NIST)
Funding: US Army, DARPA, Raytheon BBN

## Slide 23
Backup

## Slide 24: Coupled Resonator with Tunable Doublet Spacing
Out
In
Resonator 1
Resonator 2
1.5
φ
-φ
Tunable coupling (µ)
Microwave cavity
Tuning of doublet spacing allows perfect frequency matching to microwave resonance