## Slide 1: Simulating New Instruments for Direct Imaging of Exoplanets
Edwin Alexani
RIT – Monday, October 6th, 2024

## Slide 2
Why do I do what I do?
I always loved astronomy!
Where does all the data come from?
How can I help the community get more data?
Long days, but fulfilling!
Define achievable tasks to complete along the way.
Break the work in smaller chunks that fit together.
Research is not linear, it often branches!
Have a “big picture plan” to refer back to and keep research organized.
Technology gives me flexibility and transferable skills to many applications.

## Slide 3
Introduction
The Habitable Worlds Observatory and Direct Imaging
Astrophotonic Spectrographs
Single Photon Counting Detectors
Single Photon Counting Photonic Spectrograph
Astronomical Sources
Signal-to-Noise Ratio
Simulations
Results
Requirements Flow Down
Conclusion
Overview

## Slide 4: Introduction

## Slide 5: Introduction
NASA plans to launch New Great Observatories, and prioritizes the Habitable Worlds Observatory (HWO).
One of the main objectives of HWO is to directly image terrestrial exoplanets and obtain their spectra.
Direct imaging requires suppression of starlight. One way to do this using a coronagraph and/or starshade. Direct imaging also requires sensitive detectors. Spectrographs are needed for spectra.
We propose to combine CMOS single photon counting detectors (SPCD) with astrophotonic spectrographs (APS). We aim to provide a compact and sensitive instrument for space applications.

## Slide 6: Introduction
Photosynthesis is responsible for modern oxygen levels.
The O2-A band biosignature at 760nm indicates the presence of oxygen in the Earth’s atmosphere. This project focuses on its detectability.
O2-A Band

## Slide 7: The and Direct Imaging

## Slide 8: The and Direct Imaging
The Habitable Worlds Observatory (HWO) will be in space. It will have a coronagraph with 10-10 contrast. HWO draws from past designs like LUVOIR and HabEx.
LUVOIR-A [15m]
LUVOIR-B [8m]
HabEx [4m]
Starshade [52m]

## Slide 9: The and Direct Imaging
LUVOIR-B is the telescope used in this study. Its architecture and deployment method have JWST heritage.
Diameter: 8m
Throughput*: 20%
Dark Current: 3×10-5 e-/pix/s
Read Noise: 0 e-
Detector Temperature: 170 K
Inner Working Angle (IWA) = 3.5 λ/D
Outer Working Angle (OWA) = 64 λ/D
Contrast Ratio: 10-10
Instrument: ECLIPS-B
Telescope Temperature: 270 K

## Slide 10: Astrophotonic Spectrographs

## Slide 11: Astrophotonic Spectrographs (APS)
APS use AWG to create a discretized spectrum. The waveguides in the AWG have a length difference of mλ.
This light constructively interferes along the Rowland circle and give the discrete spectrum.
Source: Pradip Gatkine
Free Propagation Region (FPR)
Arrayed Waveguide Grating (AWG)
FPR
Output Waveguides
Single Mode Input Fiber
Rowland Circle
AWG
Output Spectrum

## Slide 12: Single Photon Counting Detectors

## Slide 13: Single Photon Counting Detectors
Hamamatsu
ORCA Quest
CMOS: Complementary Metal-Oxide Semiconductor.
CMOS has faster readout, per pixel (radiation tolerant). CMOS are typically Silicon devices (Vis), found in different formats, and are part of the cellphone camera industry. CMOS sensors are used in this study.
BAE HWK4123 CMOS Sensor

## Slide 14: Single Photon Counting Photonic Spectrograph

## Slide 15
Single Photon Counting Photonic Spectrograph (SPCPS)

## Slide 16: Astronomical Sources

## Slide 17: Astronomical Sources
The planet’s spectrum is the desired signal. It includes the planet’s light and the reflected starlight. This also introduces shot noise.
The star would be the highest source of shot noise, if not for the coronagraph (1010 suppression). Speckles can also appear due to the optics (not modelled here, may use random walk or linear process).
Cosmic rays limit the maximum amount of time the detector can collect light. This constrains the readout rate (not modelled).
Exozodiacal dust reflects the starlight before the starlight is suppressed by the coronagraph. Exozodiacal dust is a significant contributor to background flux. Zodiacal dust in the solar system is similar.

## Slide 18: Signal-to-Noise Ratio

## Slide 19: Signal-to-Noise Ratio: Achieved
Once the required (desired) SNR is known, the sources of noise and system parameters can be accounted for to give an integration time to reach the SNR.

## Slide 20: Simulations

## Slide 21: Simulations: Contrast Ratios and Stellar Spectrum
ExoVista returns the planet’s contrast ratio for a given orbital position, and the stellar spectrum.

## Slide 22: Simulations: ExoVista Planet Total Light
Multiplying the contrast ratios by the stellar spectrum gives the total light coming from the planet.
Notes: Multiplying the stellar flux and contrast ratios gives the planetary spectra. Again, we show earth at different times on the right, and only modern earth on the left for different stars. As I said earlier, the planets should emit about the same flux since they are modelled in the habitable zone.

## Slide 23: Simulations: ExoVista Channels
Integrating the object flux for each exoVista channel yields photoelectron numbers.
Notes: Now that we have a flux, we need to convert this into a photoelectron number. We need to integrate the flux. In the equation above, the flux F represents the results shown just before this slide. We then divide by the photon energy, multiply by the telescope throughput, the telescope collecting area, and the detector quantum efficiency, to get the correct number of photons in each ExoVista channel. This gives us photoelectron numbers, which we will need to rebin to accommodate the discrete astrophotonic spectrograph channels. We also do this for the star light, since we already had the flux data for them.

## Slide 24: Simulations: APS Channels
The photoelectron numbers are rebinned to match the astrophotonic spectrograph channels.

## Slide 25: Simulations: Exozodiacal and Zodiacal Dust
ExoVista gives a contrast ratio for the exozodiacal dust. The same treatment used for the planet is applied to the dust.
The solar system’s zodiacal dust is viewed from “within,” and is approximated as half of the exozodiacal dust.

## Slide 26: Simulations: Achieved SNR
Once the required (desired) SNR is known, the sources of noise and system parameters can be accounted for to give an integration time to reach the SNR. Hidden in the equation are detector temperature (DC) and the number of pixels used (DC, RN).

## Slide 27: Results
Notes: Let’s take a look at the results from the detector temperature and pixel number parameter space.

## Slide 28: Results
G2V Star | 1 pixel | 9 pixels | 416 pixels
Time [days] | 17.43 | 62.95 | 2381.4
SNR [70 K] | 11.71 | 17.48 | 23.73
SNR [153 K] | 10.23 | 10.58 | 10.73
SNR [170 K] | 10.00 | 10.00 | 10.00
SNR [270 K] | 4.42 | 2.98 | 2.72
The main source of noise is the dark current (temperature and number of pixels).
Each additional pixel costs 5.7 days in integration time.

## Slide 29: Requirements Flow Down

## Slide 30: Requirements Flow Down
Focal Plane
offset ~8 µm
APS
Collimating Lens
Camera Lens
Focal Plane
Sensor

## Slide 31: Requirements Flow Down

## Slide 32: Conclusion

## Slide 33: Conclusion
The simulated observations and detector parameters provide a good first order estimate for the SNR, but will be improved.
NASA wants to directly image exoplanets with the HWO.
This is challenging and will require new technologies.
CMOS single photon detectors and astrophotonic spectrographs are new, promising technologies for this application.
NASA wants to directly image exoplanets with the HWO.
This is challenging and will require new technologies.
CMOS single photon detectors and astrophotonic spectrographs are new, promising technologies for this application.
The simulated observations and detector parameters provide a good first order estimate for the SNR, but will be improved.
The SPCPS can resolve the O2-A band biosignature in ~103 hours. The preliminary design is compact and simple. The SPCPS is a promising instrument that will be further investigated.

## Slide 34: QUESTIONS
Source: Justin Gallagher
PSPSPSPSPS
SPCPS
Source: this one is me